## Slide 1: Unit 3 Wireless Transmission Fundamentals
Preeti Godabole

## Slide 2: Topics
Introduction to narrow and wideband systems;
Spread spectrum;
Frequency hopping;
Introduction to MIMO;
  MIMO Channel Capacity and diversity gain;
Introduction to OFDM; MIMO-OFDM system;
Multiple access control (FDMA, TDMA, CDMA, SDMA);
Wireless local area network;
Wireless personal area network (Bluetooth and ZigBee)

## Slide 3: Goal of WLANs is to replace office cabling, to enable tetherless access to the internet and, to introduce a higher flexibility for ad-hoc communication in, e.g., group meetings.

## Slide 4: Wireless networks
Access computing/communication services, on the move
Cellular Networks
  traditional base station infrastructure systems
Wireless LANs
  infrastructure as well as ad-hoc networks possible
  very flexible within the reception area
  low bandwidth compared to wired networks (1-10 Mbit/s)
Multihop Ad hoc Networks
  useful when infrastructure not available, impractical, or expensive
  military applications, rescue, home networking

## Slide 5: Cellular Wireless
Single hop wireless connectivity to the wired world
  Space divided into cells, and hosts assigned to a cell
  A base station is responsible for communicating with hosts/nodes in its cell
  Mobile hosts can change cells while communicating
  Hand-off occurs when a mobile host starts communicating via a new base station

## Slide 6: Evolution of cellular networks
First-generation: Analog cellular systems (450-900 MHz)
  Frequency shift keying; FDMA for spectrum sharing
  NMT (Europe), AMPS (US)
Second-generation: Digital cellular systems (900, 1800 MHz)
  TDMA/CDMA for spectrum sharing; Circuit switching
  GSM (Europe), IS-136 (US), PDC (Japan)
  <9.6kbps data rates
2.5G: Packet switching extensions
  Digital: GSM to GPRS; Analog: AMPS to CDPD
  <115kbps data rates
3G: Full-fledged data services
  High speed, data and Internet services
  IMT-2000, UMTS
  <2Mbps data rates

## Slide 7: Characteristics of wireless LANs
Advantages
  very flexible within the reception area
  Ad-hoc networks without previous planning possible
  (almost) no wiring difficulties (e.g. historic buildings, firewalls)
  more robust against disasters like, e.g., earthquakes, fire - or users pulling a plug...
Disadvantages
  typically very low bandwidth compared to wired networks (1-10 Mbit/s)
  many proprietary solutions, especially for higher bit-rates, standards take their time (e.g. IEEE 802.11)
  products have to follow many national restrictions if working wireless, it takes a vary long time to establish global solutions like, e.g., IMT-2000
  safety and security -may interfere with the equipments , eavesdropping much easier

## Slide 8: Design goals for wireless LANs
  global, seamless operation
  low power for battery use
  no special permissions or licenses needed to use the LAN
  robust transmission technology
  simplified spontaneous cooperation at meetings
  easy to use for everyone, simple management
  protection of investment in wired networks
  security (no one should be able to read my data), privacy (no one should be able to collect user profiles), safety (low radiation)
  transparency concerning applications and higher layer protocols, but also location awareness if necessary

## Slide 9: Comparison: infrared vs. radio transmission
Infrared
  uses IR diodes, diffuse light, multiple reflections (walls, furniture etc.)
Advantages
  simple, cheap, available in many mobile devices
  no licenses needed
  simple shielding possible
Disadvantages
  interference by sunlight, heat sources etc.
  many things shield or absorb IR light
  low bandwidth
Example
  IrDA (Infrared Data Association) interface available everywhere
Radio
  typically using the license free ISM band at 2.4 GHz
Advantages
  experience from wireless WAN and mobile phones can be used
  coverage of larger areas possible (radio can penetrate walls, furniture etc.)
Disadvantages
  very limited license free frequency bands
  shielding more difficult, interference with other electrical devices
Example
  WaveLAN, HIPERLAN, Bluetooth

## Slide 10: Wireless LANs
Infrared (IrDA) or radio links (Wavelan)
Advantages
  very flexible within the reception area
  Ad-hoc networks possible
  (almost) no wiring difficulties
Disadvantages
  low bandwidth compared to wired networks
  many proprietary solutions
    Bluetooth, HiperLAN and IEEE 802.11

## Slide 11: Wireless LANs vs. Wired LANs
Destination address does not equal destination location
The media impact the design
  wireless LANs intended to cover reasonable geographic distances must be built from basic coverage blocks
Impact of handling mobile (and portable) stations
  Propagation effects
  Mobility management
  Power management

## Slide 12: Infrastructure vs. Ad hoc WLANs
infrastructure network
ad-hoc network
AP
AP
AP
wired network
AP: Access Point
Source: Schiller

## Slide 13: Multi-Hop Wireless
May need to traverse multiple links to reach destination
Mobility causes route changes

## Slide 14: Mobile Ad Hoc Networks (MANET)
Do not need backbone infrastructure support
Host movement frequent
Topology change frequent
Multi-hop wireless links
Data must be routed via intermediate nodes
A
B
A
B

## Slide 15: Applications of MANETS
Military - soldiers at Kargil, tanks, planes
Disaster Management – Orissa, Gujarat
Emergency operations – search-and-rescue, police and firefighters
Sensor networks
Taxicabs and other closed communities
airports, sports stadiums etc. where two or more people meet and want to exchange documents
Presently MANET applications use 802.11 hardware
Personal area networks - Bluetooth

## Slide 16: Wireless Lan 802.11 Evolution

## Slide 17: Challenges of Wireless Communications

## Slide 18: Wireless Media
Physical layers used in wireless networks
  have neither absolute nor readily observable boundaries outside which stations are unable to receive frames are unprotected from outside signals
  communicate over a medium significantly less reliable than the cable of a wired network
  have dynamic topologies
  lack full connectivity and therefore the assumption normally made that every station can hear every other station in a LAN is invalid (i.e., STAs may be “hidden” from each other)
  have time varying and asymmetric propagation properties

## Slide 19: Limitations of the mobile environment
Limitations of the Wireless Network
                limited communication bandwidth
  frequent disconnections
  heterogeneity of fragmented networks
Limitations Imposed by Mobility
  route breakages
  lack of mobility awareness by system/applications
Limitations of the Mobile Device
  short battery lifetime
  limited capacities

## Slide 20: Wireless v/s Wired networks
Regulations of frequencies
  Limited availability, coordination is required
  useful frequencies are almost all occupied
Bandwidth and delays
  Low transmission rates
    few Kbps to some Mbps.
  Higher delays
    several hundred milliseconds
  Higher loss rates
    susceptible to interference, e.g., engines, lightning
Always shared medium
  Lower security, simpler active attacking
  radio interface accessible for everyone
  Fake base stations can attract calls from mobile phones
  secure access mechanisms important

## Slide 21: Difference Between Wired and Wireless
If both A and C sense the channel to be idle at the same time, they send at the same time.
Collision can be detected at sender in Ethernet.
Half-duplex radios in wireless cannot detect collision at sender.
A
B
C
A
B
C
Ethernet LAN
Wireless LAN

## Slide 22: Effect of mobility on protocol stack
Application
  new applications and adaptations
Transport
  congestion and flow control
Network
  addressing and routing
Link
  media access and handoff
Physical
  transmission errors and interference

## Slide 23: 802.11-based Wireless LANs Architecture and Physical Layer
The primary goal of the standard was the specification of a simple and robust WLAN which offers time-bounded and asynchronous services.
The MAC layer should be able to operate with multiple physical layers, each of which exhibits a different medium sense and transmission characteristic

## Slide 24: Components of IEEE 802.11 architecture
The basic service set (BSS) is the basic building block of an IEEE 802.11 LAN
The ovals can be thought of as the coverage area within which member stations can directly communicate
The Independent BSS (IBSS) is the simplest LAN. It may consist of as few as two stations
ad-hoc network
BSS2
BSS1

## Slide 25: 802.11 - infrastructure network
Distribution System
Portal
802.x LAN
Access
Point
802.11 LAN
BSS2
802.11 LAN
BSS1
Access
Point
Station (STA)
  terminal with access mechanisms to the wireless medium and radio contact to the access point
Basic Service Set (BSS)
  group of stations using the same radio frequency
Access Point
  station integrated into the wireless LAN and the distribution system Portal bridge to other (wired) networks
Distribution System
  interconnection network to form one logical network (EES: Extended Service Set) based on several BSS
STA1
STA2
STA3
ESS
Source: Schiller
Notes: 9

## Slide 26: 802.11 - ad-hoc network
Direct communication within a limited range
  Station (STA): terminal with access mechanisms to the wireless medium
  Basic Service Set (BSS): group of stations using the same radio frequency
802.11 LAN
BSS2
802.11 LAN
BSS1
STA1
STA4
STA5
STA2
STA3
Source: Schiller

## Slide 27: Distribution System (DS) concepts
The Distribution system interconnects multiple BSSs
802.11 standard logically separates the wireless medium from the distribution system – it does not preclude, nor demand, that the multiple media be same or different
An Access Point (AP) is a STA that provides access to the DS by providing DS services in addition to acting as a STA.
Data moves between BSS and the DS via an AP
The DS and BSSs allow 802.11 to create a wireless network of arbitrary size and complexity called the Extended Service Set network (ESS)

## Slide 28: Extended Service Set network
Source: Intersil

## Slide 29: 802.11- in the TCP/IP stack
mobile terminal
access point
server
fixed terminal
application
TCP
802.11 PHY
802.11 MAC
IP
802.3 MAC
802.3 PHY
application
TCP
802.3 PHY
802.3 MAC
IP
802.11 MAC
802.11 PHY
LLC
infrastructure network
LLC
LLC

## Slide 30: 802.11 - Layers and functions
PLCP Physical Layer Convergence Protocol
  clear channel assessment signal (carrier sense)
PMD
Physical Medium Dependent modulation, coding
PHY Management
  channel selection, MIB
Station Management
  coordination of all management functions
PMD
PLCP
MAC
LLC
MAC Management
PHY Management
MAC
  access mechanisms, fragmentation, encryption
MAC Management
  synchronization, roaming, MIB, power management
PHY
DLC
Station Management

## Slide 31: IEEE 802.11
Wireless LAN standard defined in the unlicensed spectrum (2.4 GHz and 5 GHz U-NII bands)
Standards covers the MAC sublayer and PHY layers
Three different physical layers in the 2.4 GHz band
  FHSS, DSSS and IR
OFDM based Phys layer in the 5 GHz band (802.11a)
902 MHz
928 MHz
26 MHz
83.5 MHz
200 MHz
2.4 GHz
2.4835 GHz
5.15 GHz
5.35 GHz

33cm
12cm
5cm

## Slide 32: 802.11 - Physical layer
All PHY variants include the provision of the clear channel assessment signal (CCA). This is needed for the MAC mechanisms controlling medium access and indicates if the medium is currently idle
The PHY layer offers a service access point (SAP) with 1 or 2 Mbit/s transfer
rate to the MAC layer (basic version of the standard).
3 versions of spread spectrum:
2 radio (typ. 2.4 GHz),
1 IR data rates 1 or 2 Mbps
1.FHSS (Frequency Hopping Spread Spectrum)
  spreading, despreading, signal strength, typically 1 Mbps min. 2.5 frequency hops/s (USA), two-level GFSK modulation

## Slide 33: FHSS PHY packet format
synchronization
SFD
PLW
PSF
HEC
payload
PLCP preamble
PLCP header
80
16
12
4
16
variable
bits
Synchronization
  synch with 010101... pattern
SFD (Start Frame Delimiter)
  0000110010111101 start pattern
PLW (PLCP_PDU Length Word)
  length of payload incl. 32 bit CRC of payload, PLW < 4096
PSF (PLCP Signaling Field)
  data of payload (1 or 2 Mbit/s)
HEC (Header Error Check)
  CRC with x16+x12+x5+1

## Slide 34
2.DSSS (Direct Sequence Spread Spectrum)
  DBPSK modulation for 1 Mbps (Differential Binary Phase Shift Keying), DQPSK for 2 Mbps (Differential Quadrature PSK)
  preamble and header of a frame is always transmitted with 1 Mbps, rest of transmission 1 or 2 Mbps
  chipping sequence: +1, -1, +1, +1, -1, +1, +1, +1, -1, -1, -1 (Barker code)
  max. radiated power 1 W (USA), 100 mW (EU), min. 1mW
  3.Infrared
  850-950 nm, diffuse light, typ. 10 m range
  carrier detection, energy detection, synchronization

## Slide 35: DSSS PHY packet format
synchronization
SFD
signal
service
HEC
payload
PLCP preamble
PLCP header
128
16
8
8
16
variable
bits
length
16
Synchronization
  synch., gain setting, energy detection, frequency offset compensation
SFD (Start Frame Delimiter)
  1111001110100000
Signal
  data rate of the payload (0A: 1 Mbit/s DBPSK; 14: 2 Mbit/s DQPSK)
Service Length
  future use, 00: 802.11 compliant length of the payload
HEC (Header Error Check)
  protection of signal, service and length, x16+x12+x5+1

## Slide 36: Hardware
Original WaveLAN card (NCR)
  914 MHz Radio Frequency
  Transmit power 281.8 mW
  Transmission Range ~250 m (outdoors) at 2Mbps
  SNRT 10 dB (capture)
WaveLAN II (Lucent)
  2.4 GHz radio frequency range
  Transmit Power 30mW
  Transmission range 376 m (outdoors) at 2 Mbps (60m indoors)
  Receive Threshold = - 81dBm
  Carrier Sense Threshold = -111dBm
Many others….Agere, Cisco,………

## Slide 37: 802.11-based Wireless LANs MAC functional spec - DCF

## Slide 38: 802.11 - MAC layer I - DFWMAC
Traffic services
  Asynchronous Data Service (mandatory)
    exchange of data packets based on “best-effort”
    support of broadcast and multicast
  Time-Bounded Service (optional)
    implemented using PCF (Point Coordination Function)
Access methods
  DFWMAC-DCF CSMA/CA (mandatory)
    collision avoidance via randomized „back-off“ mechanism
    minimum distance between consecutive packets
    ACK packet for acknowledgements (not for broadcasts)
  DFWMAC-DCF w/ RTS/CTS (optional)
    Distributed Foundation Wireless MAC
    avoids hidden terminal problem
  DFWMAC- PCF (optional)
    access point polls terminals according to a list

## Slide 39: 802.11 - MAC layer II
Priorities
    defined through different inter frame spaces
    no guaranteed, hard priorities
  SIFS (Short Inter Frame Spacing)
      highest priority, for ACK, CTS, polling response
  PIFS (PCF IFS)
      medium priority, for time-bounded service using PCF
  DIFS (DCF, Distributed Coordination Function IFS)
      lowest priority, for asynchronous data service
t
medium busy
SIFS
PIFS
DIFS
DIFS
next frame
contention
direct access if medium is free  DIFS

## Slide 40: 802.11 - CSMA/CA access method I
t
medium busy
DIFS
DIFS
next frame
contention window
(randomized back-off mechanism)
  station ready to send starts sensing the medium (Carrier Sense based on CCA, Clear Channel Assessment)
  if the medium is free for the duration of an Inter-Frame Space (IFS), the station can start sending (IFS depends on service type)
  if the medium is busy, the station has to wait for a free IFS, then the station must additionally wait a random back-off time (collision avoidance, multiple of slot-time)
  if another station occupies the medium during the back-off time of the station, the back-off timer stops (fairness)
slot time
direct access if medium is free  DIFS
Notes: 12

## Slide 41: 802.11 - CSMA/CA access method II
Sending unicast packets
  station has to wait for DIFS before sending data
  receivers acknowledge at once (after waiting for SIFS) if the packet was received correctly (CRC)
  automatic retransmission of data packets in case of transmission errors
t
SIFS
DIFS
data
ACK
waiting time
other
stations
receiver
sender
data
DIFS
contention

## Slide 42: 802.11 - DFWMAC
Sending unicast packets
  station can send RTS with reservation parameter after waiting for DIFS (reservation determines amount of time the data packet needs the medium)
  acknowledgement via CTS after SIFS by receiver (if ready to receive)
  sender can now send data at once, acknowledgement via ACK
  other stations store medium reservations distributed via RTS and CTS
t
SIFS
DIFS
data
ACK
defer access
other
stations
receiver
sender
data
DIFS
contention
RTS
CTS
SIFS
SIFS
NAV (RTS)
NAV (CTS)
Notes: Distributed foundation wireless MAC

## Slide 43: 802.11 - Carrier Sensing
In IEEE 802.11, carrier sensing is performed
  at the air interface (physical carrier sensing), and
  at the MAC layer (virtual carrier sensing)
Physical carrier sensing
  detects presence of other users by analyzing all detected packets
  Detects activity in the channel via relative signal strength from other sources
Virtual carrier sensing is done by sending MPDU duration information in the header of RTS/CTS and data frames
Channel is busy if either mechanisms indicate it to be
Duration field indicates the amount of time (in microseconds) required to complete frame transmission
Stations in the BSS use the information in the duration field to adjust their network allocation vector (NAV)

## Slide 44: 802.11 - Collision Avoidance
If medium is not free during DIFS time..
Go into Collision Avoidance: Once channel becomes idle, wait for DIFS time plus a randomly chosen backoff time before attempting to transmit
For DCF the backoff is chosen as follows:
  When first transmitting a packet, choose a backoff interval in the range [0,cw]; cw is contention window, nominally 31
  Count down the backoff interval when medium is idle
  Count-down is suspended if medium becomes busy
  When backoff interval reaches 0, transmit RTS
  If collision, then double the cw up to a maximum of 1024
Time spent counting down backoff intervals is part of MAC overhead

## Slide 45: 802.11 - Congestion Control
Contention window (cw) in DCF: Congestion control achieved by dynamically choosing cw
large cw leads to larger backoff intervals
small cw leads to larger number of collisions
Binary Exponential Backoff in DCF:
  When a node fails to receive CTS in response to its RTS, it increases the contention window
    cw is doubled (up to a bound cwmax =1023)
  Upon successful completion data transfer, restore cw to cwmin=31

## Slide 46: 802.11 - Frame format
Types
  control frames, management frames, data frames
Sequence numbers
  important against duplicated frames due to lost ACKs
Addresses
  receiver, transmitter (physical), BSS identifier, sender (logical)
Miscellaneous
  sending time, checksum, frame control, data
Frame
Control
Duration
ID
Address
1
Address
2
Address
3
Sequence
Control
Address
4
Data
CRC
2
2
6
6
6
6
2
4
0-2312
bytes
version, type, fragmentation, security, ...

## Slide 47: Types of Frames
Control Frames
  RTS/CTS/ACK
  CF-Poll/CF-End
Management Frames
  Beacons
  Probe Request/Response
  Association Request/Response
  Dissociation/Reassociation
  Authentication/Deauthentication
  ATIM
Data Frames

## Slide 48: 802.11 - MAC management
Synchronization
  try to find a LAN, try to stay within a LAN timer etc.
Power management
  sleep-mode without missing a message
  periodic sleep, frame buffering, traffic measurements
Association/Reassociation
  integration into a LAN
  roaming, i.e. change networks by changing access points
  scanning, i.e. active search for a network
MIB - Management Information Base
  managing, read, write

## Slide 49: 802.11 - Synchronization
All STAs within a BSS are synchronized to a common clock
  Infrastructure mode: AP is the timing master
    periodically transmits Beacon frames containing Timing Synchronization function (TSF)
    Receiving stations accepts the timestamp value in TSF
  Ad hoc mode: TSF implements a distributed algorithm
    Each station adopts the timing received from any beacon that has TSF value later than
    its own TSF timer
This mechanism keeps the synchronization of the TSF timers in a BSS to within 4 s plus the maximum propagation delay of the PHY layer

## Slide 50: Synchronization using a Beacon (infrastructure)
beacon interval
t
medium
access
point
busy
B
busy
busy
busy
B
B
B
value of the timestamp
B
beacon frame

## Slide 51: Synchronization using a Beacon (ad-hoc)
t
medium
station1
busy
B1
beacon interval
busy
busy
busy
B1
value of the timestamp
B
beacon frame
station2
B2
B2
random delay

## Slide 52: Power management
Idea: switch the transceiver off if not needed
States of a station: sleep and awake
Timing Synchronization Function (TSF)
  stations wake up at the same time
Infrastructure
    Traffic Indication Map (TIM)
      list of unicast receivers transmitted by AP
    Delivery Traffic Indication Map (DTIM)
      list of broadcast/multicast receivers transmitted by AP
Ad-hoc
    Ad-hoc Traffic Indication Map (ATIM)
      announcement of receivers by stations buffering frames
      more complicated - no central AP
      collision of ATIMs possible (scalability?)

## Slide 53: Power saving with wake-up patterns (infrastructure)
TIM interval
t
medium
access
point
busy
D
busy
busy
busy
T
T
D
T
TIM
D
DTIM
DTIM interval
B
B
B
broadcast/multicast
station
awake
p
PS poll
p
d
d
d
data transmission
to/from the station

## Slide 54: Power saving with wake-up patterns (ad-hoc)
awake
A
transmit ATIM
D
transmit data
t
station1
B1
B1
B
beacon frame
station2
B2
B2
random delay
A
a
D
d
ATIM
window
beacon interval
a
acknowledge ATIM
d
acknowledge data

## Slide 55: 802.11 - Roaming
No or bad connection? Then perform:
Scanning
  scan the environment, i.e., listen into the medium for beacon signals or send probes into the medium and wait for an answer
Reassociation Request
  station sends a request to one or several AP(s)
Reassociation Response
  success: AP has answered, station can now participate
  failure: continue scanning
AP accepts Reassociation Request
  signal the new station to the distribution system
  the distribution system updates its data base (i.e., location information)
  typically, the distribution system now informs the old AP so it can release resources

## Slide 56: IEEE 802.11 Summary
Infrastructure and ad hoc modes using DCF
Carrier Sense Multiple Access
Binary exponential backoff for collision avoidance and congestion control
Acknowledgements for reliability
Power save mode for energy conservation
Time-bound service using PCF
Signaling packets for avoiding Exposed/Hidden terminal problems, and for reservation
    Medium is reserved for the duration of the transmission
    RTS-CTS in DCF
    Polls in PCF

## Slide 57
IEEE WPAN (Wireless Personal Area Networks)
  market potential
  compatibility
  low cost/power, small form factor
  technical/economic feasibility
    Bluetooth
    Zigbee

## Slide 58: Bluetooth
Idea
Universal radio interface for ad-hoc wireless connectivity
Interconnecting computer and peripherals, handheld devices, PDAs, cell phones – replacement of IrDA
Embedded in other devices, goal: 5€/device (2005: 40€/USB bluetooth)
Short range (10 m), low power consumption, license-free 2.45 GHz ISM
Voice and data transmission, approx. 1 Mbit/s gross data rate
One of the first modules (Ericsson).
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/

## Slide 59: Bluetooth
History
1994: Ericsson (Mattison/Haartsen), “MC-link” project
Renaming of the project: Bluetooth according to Harald “Blåtand” Gormsen [son of Gorm], King of Denmark in the 10th century
1998: foundation of Bluetooth SIG, www.bluetooth.org
1999: erection of a rune stone at Ercisson/Lund ;-)
2001: first consumer products for mass market, spec. version 1.1 released
2005: 5 million chips/week
Special Interest Group
Original founding members: Ericsson, Intel, IBM, Nokia, Toshiba
Added promoters: 3Com, Agere (was: Lucent), Microsoft, Motorola
> 2500 members
Common specification and certification of products
(was:
)
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/

## Slide 60: Characteristics
  GHz ISM band, 79 (23) RF channels, 1 MHz carrier spacing
    Channel 0: 2402 MHz … channel 78: 2480 MHz
    G-FSK modulation, 1-100 mW transmit power
FHSS and TDD
    Frequency hopping with 1600 hops/s
    Hopping sequence in a pseudo random fashion, determined by a master
    Time division duplex for send/receive separation
Voice link – SCO (Synchronous Connection Oriented)
    FEC (forward error correction), no retransmission, 64 kbit/s duplex, point- to-point, circuit switched
Data link – ACL (Asynchronous ConnectionLess)
    Asynchronous, fast acknowledge, point-to-multipoint, up to 433.9 kbit/s symmetric or 723.2/57.6 kbit/s asymmetric, packet switched
Topology
    Overlapping piconets (stars) forming a scatternet
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/

## Slide 61: Piconet
Collection of devices connected in an ad hoc fashion
One unit acts as master and the others as slaves for the lifetime of the piconet
Master determines hopping pattern, slaves have to synchronize
Each piconet has a unique hopping pattern
Participation in a piconet = synchronization to hopping sequence
Each piconet has one master and up to 7 simultaneous slaves (> 200 could be parked)
M=Master S=Slave
P=Parked SB=Standby
M
S
P
SB
S
S
P
P
SB
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/

## Slide 62: Forming a piconet
All devices in a piconet hop together
Master gives slaves its clock and device ID
  Hopping pattern: determined by device ID (48 bit, unique worldwide)
  Phase in hopping pattern determined by clock
Addressing
Active Member Address (AMA, 3 bit)
Parked Member Address (PMA, 8 bit)
SB
SB
SB
SB
SB
SB
SB
SB
SB
M
S
P
SB
S
S
P
P
SB












 



Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/

## Slide 63: Scatternet
Linking of multiple co-located piconets through the sharing of common master or slave devices
Devices can be slave in one piconet and master of another
Communication between piconets
Devices jumping back and forth between the piconets
M=Master S=Slave P=Parked SB=Standby
M
S
P
SB
S
S
P
P
SB
M
S
S
P
SB
Piconets (each with a capacity of 720 kbit/s)
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/

## Slide 64: Bluetooth protocol stack
Baseband
Radio
Link Manager
Control
Host Controller Interface
Logical Link Control and Adaptation Protocol (L2CAP)
Audio
TCS BIN SDP
OBEX
vCal/vCard
IP
NW apps.
TCP/UDP
RFCOMM (serial line interface)
AT modem commands
telephony apps.
audio apps.
mgmnt. apps.
AT: attention sequence OBEX: object exchange
TCS BIN: telephony control protocol specification – binary
BNEP: Bluetooth network encapsulation protocol
SDP: service discovery protocol RFCOMM: radio frequency comm.
BNEP PPP
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/

## Slide 65: Bluetooth Protocol Stack
Radio: Specification of the air interface, i.e., frequencies, modulation, and transmit power
Baseband: Description of basic connection establishment, packet formats, timing, and basic QoS parameters
Link manager protocol: Link set-up and management between devices including security functions and parameter negotiation
Logical link control and adaptation protocol (L2CAP): Adaptation of higher layers to the baseband (connectionless and connection-oriented services,
Service discovery protocol: Device discovery in close proximity plus querying of service characteristics

## Slide 66: Bluetooth Protocol Stack
Cable replacement protocol RFCOMM that emulates a serial line interface following the EIA-232 (formerly RS-232) standards. RFCOMM supports multiple serial ports over a single physical channel.
The telephony control protocol specification – binary (TCS BIN) describes a bit-oriented protocol that defines call control signaling for the establishment of voice and data calls between Bluetooth devices. It also describes mobility and group management functions. The host controller interface (HCI) between the baseband and L2CAP provides a command interface to the baseband controller and link manager, and access to the hardware status and control registers. The HCI can be seen as the hardware/software boundary.

## Slide 67: L2CAP - Logical Link Control and Adaptation Protocol
Simple data link protocol on top of baseband
Connection oriented, connectionless, and signalling channels Protocol multiplexing
RFCOMM, SDP, telephony control
Segmentation & reassembly
Up to 64kbyte user data, 16 bit CRC used from baseband
QoS flow specification per channel
Follows RFC 1363, specifies delay, jitter, bursts, bandwidth
Group abstraction
Create/close group, add/remove member
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/

## Slide 68: Security architecture of Bluetooth
E3
E2
link key (128 bit)
encryption key (128 bit)
payload key
Keystream generator
Data
Data
Authentication key generation (possibly permanent storage)
Encryption key generation (temporary storage)
PIN (1-16 byte)
User input (initialization) Pairing
Authentication
Encryption
Ciphering
Cipher data
E3
E2
link key (128 bit)
encryption key (128 bit)
payload key
Keystream generator
PIN (1-16 byte)
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/

## Slide 69: LMP
Authentication, pairing, and encryption: Although basic authentication is handled in the baseband, LMP has to control the exchange of random numbers and signed responses.
Synchronization: Precise synchronization is of major importance within a Bluetooth network. The clock offset is updated each time a packet is received from the master. Additionally, special synchronization packets can be received.
Capability negotiation: Not all Bluetooth devices will support all features that are described in the standard, so devices have to agree the usage of, e.g., multi-slot packets, encryption, SCO links, voice encoding, park/sniff/hold mode (explained below), HV2/HV3 packets etc.
Quality of service negotiation: Different parameters control the QoS of a Bluetooth device at these lower layers. The poll interval, i.e., the maximum time between transmissions from a master to a particular slave, controls the latency and transfer capacity. Depending on the quality of the channel, DM or DH packets may be used (i.e., 2/3 FEC protection or no protection).
Power control: A Bluetooth device can measure the received signal strength. Depending on this signal level the device can direct the sender of the measured signal to increase or decrease its transmit power.

## Slide 70: SDP – Service Discovery Protocol
Inquiry/response protocol for discovering services
Searching for and browsing services in radio proximity
Adapted to the highly dynamic environment
Can be complemented by others like SLP, Jini, Salutation, …
Defines discovery only, not the usage of services
Caching of discovered services
Gradual discovery
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/

## Slide 71: Additional protocols to support legacy protocols/apps.
RFCOMM
Emulation of a serial port (supports a large base of legacy applications)
Allows multiple ports over a single physical channel
Telephony Control Protocol Specification (TCS)
Call control (setup, release)
Group management
OBEX
Exchange of objects, IrDA replacement
WAP
Interacting with applications on cellular phones
Prof. Dr.-Ing. Jochen Schiller, http://www.jochenschiller.de/

## Slide 72: Power management
. All devices being active must have the 3-bit active member address (AMA).
To save battery power, a Bluetooth device can go into one of three low power states:
  Sniff state: The sniff state has the highest power consumption of the low power states. Here, the device listens to the piconet at a reduced rate (not on every other slot as is the case in the active state).
  Hold state: The device does not release its AMA . If there is no activity in the piconet, the slave may either reduce power consumption or participate in another piconet.
  Park state: In this state the device has the lowest duty cycle and the lowest power consumption. The device releases its AMA and receives a parked member address (PMA). The device is still a member of the piconet, but gives room for another device to become active

## Slide 73: Zigbee
Zigbee is a standards-based wireless technology developed to enable low-cost, low-power wireless machine-to-machine (M2M) and internet of things (IoT) networks.
Zigbee is for low-data rate, low-power applications and is an open standard.
Zigbee products have been extended and customized by vendors and, thus, plagued by interoperability issues.
In contrast to Wi-Fi networks used to connect endpoints to high-speed networks, Zigbee supports much lower data rates and uses a mesh networking protocol to avoid hub devices and create a self-healing architecture.
IEEE 802.15.4 wireless standard for wireless personal area networks (WPANs). The Zigbee WPANs operate on 2.4 Ghz, 900 MHz and 868 MHz frequencies.

## Slide 74: ZigBee Architecture
Zigbee Applications:
Home Automation
Medical Data Collection
Industrial Control Systems
meter reading system
light control system

## Slide 75: Bluetooth v/s Zigbee
Bluetooth was developed under IEEE 802.15.1, which is used for providing wireless communication through radio signals. The frequency range supported in Bluetooth varies from 2.4 GHz to 2.483 GHz. It covers less distance than Zigbee. In Bluetooth, GFSK modulation technique is used.
Zigbee, BPSK and QPSK modulation techniques are used like UWB (Ultra-Wide Band). the frequency range supported in Zigbee is mostly 2.4 GHz worldwide, which means 2.4 GHz is not supported at all times. It covers more distance as compared with Bluetooth.
Bluetooth networks can be built using the point-to-point master-slave approach in which there is one master and up to seven slaves form a piconet, which leads to forming a scatter net which is a linking of two or more piconets. | Zigbee devices can be networked in a variety of generic topologies, including a star, mesh, and others. A cluster can be created by connecting different Zigbee-based network topologies. Zigbee Coordinator, Zigbee Router, and Zigbee Endpoint nodes make up any Zigbee network.