## Slide 2
A laser is a device that generates light by a process called STIMULATED EMISSION.
A laser is a device that can produce a very narrow intense beam of monochromatic coherent light.
Light Amplification by Stimulated Emission of Radiation- (LASER).

## Slide 3
Properties of Laser Light
Monochromaticity
  Laser light is concentrated in a narrow range of wavelengths
Coherence
  All the emitted photons bear a constant phase relationship with each other in both time and phase
Directionality
  laser light is usually low in divergence
High Irradiance
  light possesses high radiant power per unit area

## Slide 4
E1
E2
Absorption

## Slide 5
Spontaneous Emission

## Slide 6
Stimulated Emission
The emitted photon is identical in all respects to the incident photon. Its frequency is same. It is in the same phase with the incident photon. Both photons travels in the same direction and are in the same state of polarization

## Slide 7
Atoms in an excited state can be stimulated to jump to a lower energy level when they are struck by a photon of incident light whose energy is the same as the energy-level difference involved in the jump. The electron thus emits a photon of the same wavelength as the incident photon. The incident and emitted photons travel away from the atom in phase.
This process is called stimulated emission.

## Slide 9
Einstein’s coefficients
Einstein calculated the probability of
absorption, spontaneous emission
and stimulated emission
Probability of absorption
(P12)ab =r(n) B12
B12 = Einstein’s coefficient for absorption
Probability of Spontaneous emission
(P21)sp =A21
A21 = Einstein’s coefficient for spontaneous emission
Probability of Stimulated emission
(P21)st = r(n) B21
B21 = Einstein’s coefficient for stimulated emission
r(n) = photon density
E1
E2

## Slide 10
Number of absorption at any instant of time Δt is given as,
Nab = N1r(n) B12 Δt
( N1- No of atoms at E1)
Number of spontaneous emission at any instant of time Δt is given as,
(P21)sp = N2 A21 Δt
( N2- No of atoms at E2)
Number of stimulated emission at any instant of time Δt is given as,
(P21)st = N2 r(n) B21 Δt

## Slide 11: Relationship between the Einstein Coefficients
To establish the relationship between Einstein Coefficient few assumptions are made:
The atoms and the radiation are in thermal equilibrium.
The radiation is identical with black body radiation and consistent with Planck's radiation law for any value of T.
The population densities N1 and N2 at the lower and upper energy levels respectively are constant in time and are distributed according to Boltzmann law in the energy levels.
Under thermal equilibrium,
Number of upward transition = Number of downward transition
Nab = Nsp + Nst
N1 r(n) B12 Δt = N2 r(n) A21 Δt + N2 r(n) B21 Δt
r(n)[B12 . N1 - B21. N2] = A21 .N2
r(n) = [A21 . N2] / [B12 . N1 - B21. N2]
Divide numerator and denominator by B21. N2
=

## Slide 12
From Boltzmann’s equation
Hence
From Plank’s energy distribution formula
Hence A21 / B21 =
and B12 / B21 = 1
and B21 = B12 = (c3/ 8πh ). A21
Einstein coefficient Relationship

## Slide 13: Light Amplification
Conditions under which the number of stimulated transitions can be made larger than the other two transition:
Condition for stimulated emission to dominate spontaneous emission
- Population Inversion
Requirement of states of larger lifetimes
- Metastable States
Condition for stimulated emission to dominate absorption transition
- Confining Radiation within the medium

## Slide 14
Power Supply
Lasing Medium
      - gas, solid or liquid material that generates laser light
Pumping Device
      - creates population inversion essential for laser operation
Optical Resonant Cavity
      - chamber where population inversion occurs that contains reflecting surfaces

## Slide 15: Lasing Action
Step 1: Pumping
- The atoms in the medium are in ground state initially. By supplying energy from an external source, the atoms are excited from the ground level to an excited state.
Step 2: Population Inversion
- The lifetime of atoms at excited state is extremely small, of the order of 10-8 sec. Therefore, the atoms drop spontaneously from the exited state to the metastable state is comparatively longer (10-3 sec), the atoms go on accumulating at the metastable state. As soon as a the number of atoms at the metastable state exceed that of the ground state, the medium goes into the state of population inversion.
Step 3: Spontaneous Emissions
- Some of the excited atoms at the metastable state may emit photos spontaneously. Each spontaneous photon can trigger many stimulated transitions along the direction of its propagation.
Step 4: Amplification
- A majority of photons traveling along the axis cause stimulated emission and are reflected back on reaching the end mirror. They travel towards the opposite mirror and on their way stimulate more and more atoms .
Step 5: Oscillations
- For proper build up of oscillations, it is essential that the amplification between two consecutive reflections of light from rear end mirror can balance the losses. Strong laser beam emerge out.

## Slide 16: Components of laser
Active Medium
The Pump
Optical Resonator
Schematic diagram of Laser

## Slide 17
When a sizable population of electrons resides in upper levels, this condition is called a "population inversion", and it sets the stage for stimulated emission of multiple photons. This is the precondition for the light amplification which occurs in a LASER and since the emitted photons have a definite time and phase relation to each other, the light has a high degree of coherence.

## Slide 18
In order to obtain the coherent light from stimulated
emission, two conditions must be satisfied:
The atoms must be excited to the higher state. That is, an inverted population is needed, one in which more atoms are in the upper state than in the lower one, so that emission of photons will dominate over absorption.
Unexcited system
Excited system
Inverted Population

## Slide 19
Mirror
Mirror
Population inversion
Population inversion can be created by introducing a so call metastable centre where electrons can piled up to achieve a situation where more N2 than N1
The process of attaining a population inversion is called pumping and the objective is to obtain a non-thermal equilibrium.
It is not possible to achieve population inversion with a 2-state system.
If the radiation flux is made very large the probability of stimulated emission and absorption can be made far exceed the rate of spontaneous emission.
But in 2-state system, the best we can get is N1 = N2.
To create population inversion, a 3-state system is required.
The system is pumped with radiation of energy E31 then atoms in state 3 relax to state 2 non radiatively.
The electrons from E2 will now jump to E1 to give out radiation.

## Slide 20
Metastable State
2. The higher state must be a metastable state – a state in which the electrons remain longer than usual so that the transition to the lower state occurs by stimulated emission rather than spontaneously.
Metastable state
Photon of energy
Metastable system
Stimulated emission
Incident photon
Emitted photon

## Slide 21
Mirror
Mirror
Spontaneous émission (production of chance photon)

## Slide 22
Mirror
Mirror
Stimulated emission
Optical Resonator

## Slide 23
Mirror
Mirror
Feed-back by the cavity

## Slide 24
Mirror
Mirror
Stimulated emission

## Slide 25
Mirror
Mirror
Feed-back by the cavity

## Slide 26
Mirror
Mirror
After several round trips…
Laser beam
Photons with:
- same energy : Monochromatic
- same direction of propagation : Spatial cohérence
- all in synchrony: Temporal cohérence

## Slide 27
Optical Resonator

## Slide 28: Pumping
In order to invert population of atomic levels the atoms must be excited by depositing energy in the medium using such method as to to increase the number of atoms at the upper level N2 and decrease the number of atoms at the lower level N1. This process is called pumping since the atoms are redistributed as if pumped from the lower level to the upper level.
The methods of pumping are
i) optical pumping, where the atoms are excited by illumination of light
ii) excitation by electric discharge in the case of gases
iii) Injection of carriers by a forward current through a p-n junction in the case of semi-conductors
iv) excitation by irradiation with electron beams
v) excitation by chemical reaction

## Slide 29
Types of Lasers
Classified according to the nature of material between two reflecting surfaces
  Solid State laser or Crystal lasers
    synthetic ruby (aluminum oxide and chromium)
    neodymium, yttrium, aluminum, garnet (Nd:YAG)
  Gas lasers
    helium neon (HeNe)
    argon
    carbon dioxide (CO2)

## Slide 30
Low- Vs. High-Power Lasers
High power lasers = "hot" lasers
  Generate thermal responses
  used in medicine for surgical cutting and coagulation, ophthalmological, dermatological, oncological and vascular specialties
Low power lasers = “cold” lasers
  Produce a maximal output of less than 1 mW
  Cause photo-chemical rather than thermal effects

## Slide 31
Rod length 2 – 20 cm; 0.1 – 2 cm diameter
RUBY LASER
Diagram of Ruby Laser

## Slide 32
Construction
A ruby laser is a solid-state laser that uses a synthetic ruby crystal as its gain medium.
The ruby mineral (corundum) is aluminum oxide with a small amount(about 0.05%) of chromium which gives it its characteristic pink or red color by absorbing green and blue light. The ruby laser is used as a pulsed laser, producing red light at 694.3 nm.
The rod's ends had to be polished, such that one end is 100% reflecting and other end is partially reflecting.
A xenon lamp is rolled over ruby rod and is used for pumping ions to excited state. After receiving a pumping flash from the flash tube, the laser light emerges for as long as the excited atoms persist in the ruby rod, which is typically about a millisecond.

## Slide 33
Three level laser
E1
E3
E2
Fast transition
E1E3 pumping
spontaneous emission E3 E2.
state E2 is a metastable state
population inversion between states E2 and E1.
stimulated emission between E2 to E1.

## Slide 34
Working of ruby laser
Ruby laser is based on three energy levels. The upper energy level E3 I short-lived, E1 is ground state, E2 is metastable state with lifetime of 0.003 sec.

## Slide 35
When a flash of light falls on ruby rod, radiations of wavelength 5500 are absorbed by Cr3+ which are pumped to E3.

## Slide 36
The ions after giving a part of their energy to crystal lattice decay to E2 state undergoing radiation less transition.
Metastable state
In metastable state , the concentration of ions increases while that of E1 decreases. Hence, population inversion is achieved.

## Slide 37
A spontaneous emission photon by Cr3+ ion at E2 level initiates the stimulated emission by other Cr3+ ions in metastable state
Metastable state
1.79 eV

## Slide 38
Application of Ruby Laser
Ruby lasers have declined in use with the discovery of better lasing media. They are still used in a number of applications where short pulses of red light are required. Holographers around the world produce holographic portraits with ruby lasers, in sizes up to a meter squared.
Many non-destructive testing labs use ruby lasers to create holograms of large objects such as aircraft tires to look for weaknesses in the lining.
Ruby lasers were used extensively in tattoo and hair removal

## Slide 39
Drawbacks of Ruby laser
The laser requires high pumping power because the laser transition terminates at the ground state and more than half of ground state atoms must be pumped to higher state to achieve population inversion.
The efficiency of ruby laser is very low because only green component of the pumping light is used while the rest of components are left unused.
The laser output is not continuous but occurs in the form of pulses of microseconds duration.
The defects due to crystalline imperfection are also present in this laser.

## Slide 40: Nd:YAG Laser

## Slide 41
Nd: YAG Laser (Doped insulator laser) :
Lasing medium :
The host medium for this laser is Yttrium Aluminium Garnet (YAG = Y3 Al5 O12) with 1.5% trivalent neodymium ions (Nd3+) present as impurities.
The (Nd3+) ions occupy the lattice sites of yttrium ions as substitutional impurities and provide the energy levels for both pumping and lasing transitions.

## Slide 42
Contd.
When an (Nd3+) ion is placed in a host crystal lattice it is subjected to the electrostatic field of the surrounding ions, the so called crystal field.
The crystal field modifies the transition probabilities between the various energy levels of the Nd3+ ion so that some transitions, which are forbidden in the free ion, become allowed.

## Slide 44
The length of the Nd: YAG laser rod various from 5cm to 10cm depending on the power of the laser and its diameter is generally 6 to 9 mm.
The laser rod and a linear flash lamp are housed in a elliptical reflector cavity
Since the rod and the lamp are located at the foci of the ellipse, the light emitted by the lamp is effectively coupled to the rod.
The ends of the rod are polished and made optically flat and parallel.

## Slide 45
Contd.
The optical cavity is formed either by silvering the two ends of the rod or by using two external reflecting mirrors.
One mirror is made hundred percent reflecting while the other mirror is left slightly transmitting to draw the output
The system is cooled by either air or water circulation.

## Slide 47
This laser system has two absorption bands (0.73 m and 0.8 m)
Optical pumping mechanism is employed.
Laser transition takes place between two laser levels at 1.06 mm.

## Slide 48
OUTPUT CHARACTERISTICS :
The laser output is in the form of pulses with higher repetition rate
Xenon flash lamps are used for pulsed output.
Nd: YAG laser can be operated in CW mode also using tungsten-halide incandescent lamp for optical pumping.
Continuous output powers of over 1KW are obtained.

## Slide 49
Note: Nd: Glass laser :
Glass acts as an excellent host material for neodymium.
As in YAG, within the glass also local electric fields modify the Nd3+ ion energy levels.
Since the line width is much broader in glass than in YAG for Nd3+ ions, the threshold pump power required for laser action is higher.
Nd: Glass lasers are operated in the pulsed mode at wavelength 1.06 m

## Slide 50
Nd:YAG/ Nd: Glass laser applications :
These lasers are used in many scientific applications which involve generation of other wavelengths of light.
The important industrial uses of YAG and glass lasers have been in materials processing such as welding, cutting, drilling.
Since 1.06 m wavelength radiation passes through optical fibre without absorption, fibre optic endoscopes with YAG lasers are used to treat gastrointestinal bleeding.

## Slide 51
Contd.
YAG beams penetrate the lens of the eye to perform intracular procedures.
YAG lasers are used in military as range finders and target designators.

## Slide 52
Calculate the wavelength of emission from GaAs semiconductor laser whose band gap energy is 1.44 ev (plank’s constant is 6.625 x 10-34 Js and charge of an electron is 1.6 x 10-19 C. Given data : Band gap energy Eg = 1.44 ev (or) 1.44 x 1.6 x 10-19 Joules. Solution : We know Band gap energy (Eg) = h (or) hc/ we can write  = hc/Eg  = 6.625 x 10-34 x 3 x 108) / (1.44 x 1.6 x 10-19) = 8.6263 x 10-7 m = 8626.3 x 10-10 m  wave length of GaAs laser = 8626.3 Ao

## Slide 53
The carbon dioxide laser is a four level molecular laser and operates at 10.6 μm in far IR region.
The tube is filled with a mixture of carbon dioxide, nitrogen and helium in 1:4:5 proportions which constitute a lasing medium.
The active center are CO2 molecules lasing on the trnsitions between the vibrational levels of the electronic ground state.
CO2 laser
Construction
Working
When current passes through the mixture of gases, the N2 molecules get excited to the metastable state.
The excited N2 molecules cannot spontaneously lose their energy and consequently, the number of N2 molecules at the metastable level builds up.
The N2 molecules undergo inelastic collisions with ground state CO2 molecules and excite them to E5 level. Some of the CO2 molecules are also excited to the upper level E5 through collisions with electron.

## Slide 54
Vibration levels
Energy storage
Bending mode
Symmetric Stretching mode
Asymmetric Stretching mode: (001) 0.3eV
Vibrational energy:
Rotational energy:
CO2 Lasers Theory

## Slide 57
Schematic of a carbon dioxide laser

## Slide 58
Energy levels of nitrogen and carbon dioxide molecules and transition between the levels

## Slide 59: Working
When an electric discharge occurs in the gas, the electrons collide with nitrogen molecules and they are raised to excited states. This process is represented by the equation
N2 + e* = N2*
N2 = Nitrogen molecule in ground state e* = electron with kinetic energy, N2* = nitrogen molecule in excited state.
Now N2 molecules in the excited state collide with CO2 atoms in ground state and excite to higher electronic, vibrational and rotational levels.
This process is represented by the equation N2* + CO2 = CO2* + N2
N2* = Nitrogen molecule in excited state. CO2 = Carbon dioxide atoms in ground state
CO2* = Carbon dioxide atoms in excited state. N2 = Nitrogen molecule in ground state.
Since the excited level of nitrogen is very close to the E5 level of CO2 atom, population in E5 level increases.
As soon as population inversion is reached, any of the spontaneously emitted photon will trigger laser action in the tube.
There are two types of laser transition possible.
  Transition E5 to E4 :
  This will produce a laser beam of wavelength 10.6μm
  Transition E5 to E3
  This transition will produce a laser beam of wavelength 9.6μm. Normally 10.6μm transition is more intense than 9.6μm transition. The power output from this laser is 10kW.
  The carbon dioxide laser usually produces a beam that is invisible to the naked eye, but can go through the atmosphere so that it can be used as a cutting or welding device in industry.

## Slide 60
The exited state of nitrogen molecule is metastable and is identical in energy to (001) vibrational level of CO2 molecule. When current passes through the mixture of gases, the N2 molecules get exited to the metastable state, which cannot spontaneously loose their energy. Hence the number of N+ molecules in the metastable state build up. These N2 molecule suffer inelastic collision with CO2 molecule in the ground state and excite them to E5 level. Also some CO2 molecules suffer collision with electrons exited to E5 level.
In the energy level diagram E5 is the upper energy level and E3 and E4 are the lower energy levels. The necessary population inversion is achieved between E5 level and E3 and E4 levels.
The laser transition E5 to E4 produces IR radiations at10.6 μm and E5 to E3 produces IR radiations at 9.6 μm.
E3 and E4 are metastable state and from which transition occurs to E2 through inelastic collisions with unexcited CO2 molecules, which increases population of E2 The presence of He with CO2 helps to reduce population density at E2. It deexcite CO2 molecules to E1 through inelastic collision

## Slide 61: Uses of Laser (1)
In medicine
  to break up gallstones and kidney stones,
  to weld broken tissue (e.g. detached retina)
  to destroy cancerous and precancerous cells; at the same time, the heat seal off capillaries,
  to remove plaque clogging human arteries.

## Slide 62: Uses of Laser (2)
In industry
  drilling
  for welding and machining,
  Hardening – Heat treatment to harden metals in tooling and automotive industry.
  Electronic industry – It is used in manufacturing of electronic component and integrated circuits.

## Slide 63: Uses of laser (3)
In everyday life
  to be used as bar-code readers,
  to be used in compact disc players,
  to produce short pulses of light used in digital communications,
  to produce holograms.

## Slide 64: Holography
Holography is the production of holograms by the use of laser.
A hologram is a 3D image recorded in a special photographic plate.
The image appears to float in space and to move when the viewer moves.
In laser holography, the hologram is recorded using a source of laser light, which is very pure in its color and orderly in its composition.
Various setups may be used, and several types of holograms can be made, but all involve the interaction of light coming from different directions and producing a microscopic interference pattern which a plate, film, or other medium photographically records.