## Slide 1: Principles of Electrical Engineering: Electrostatics
Prepared by,
Prof. Divyang S. Jadav
(Assistant Professor, STME)

## Slide 2: What is Electrostatics?
The branch of engineering which deals with charges at rest is called electrostatics.
When a glass rod is rubbed with silk and then separated, the former becomes positively charged and the latter attains equal negative charge. It is because during rubbing, some electrons are transferred from glass to silk. Since glass rod and silk are separated by an insulating medium (i.e., air), they retain the charges. In other words, the charges on them are static or stationary.
Note that the word ‘electrostatic’ means electricity at rest.

## Slide 3: Importance/ Applications of Electrostatics
Electrostatic generators can produce voltages as high as 106 volts. Such high voltages are required for X-ray work and nuclear bombardment.
We use principles of electrostatics for spray of paints, powder, etc.
The principles of electrostatics are used to prevent pollution.
The problems of preventing sparks and breakdown of insulators in high voltage engineering are essentially electrostatic.
The development of lightning rod and capacitor are the outcomes of electrostatics.

## Slide 4: Methods of Charging a Conductor
An uncharged conductor can be charged by the following two methods : (i) By conduction (ii) By induction
By Conduction

## Slide 5: Methods of Charging a Conductor
By Induction

## Slide 6: Absolute and Relative Permittivity
Permittivity is the property of a medium and affects the magnitude of force between two point charges. The greater the permittivity of a medium, the lesser the force between the charged bodies placed in it and vice-versa.
Air or vacuum has a minimum value of permittivity. The absolute (or actual) permittivity ε0 (Greek letter ‘epsilon’) of air or vacuum is 8·854 × 10−12 F/m. The absolute (or actual) permittivity ε of all other insulating materials is greater than ε0. The ratio ε/ε0 is called the relative permittivity of the material and is denoted by εr i.e.

## Slide 7: Electric Field
The region surrounding a charged body is always under stress and strain because of the electrostatic charge.
If a small charge is placed in this region, it will experience a force according to Coulomb’s laws. This stressed region around a charged body is called electric field.
Theoretically, electric field due to a charge extends upto infinity but its effect practically dies away very quickly as the distance from the charge increases.
The space (or field) in which a charge experiences a force is called an electric field or electrostatic field.

## Slide 8: Electric Field
The electric field around a charged body is represented by imaginary lines, called electric lines of force.
By convention, the direction of these lines of force at any point is the direction along which a unit positive charge (i.e., positive charge of 1C) placed at that point would move or tend to move.
The unit positive charge is sometimes called a test charge because it is used as an indicator to find the direction of electric field.
Following this convention, it is clear that electric lines of force would always originate from a positive charge and end on a negative charge.
The electric lines of force leave or enter the charged surface normally.

## Slide 9: Electric Field

## Slide 10: Properties of Electric Lines of Force
The electric field lines are directed away from a positive charge and towards a negative charge so that at any point, the tangent to a field line gives the direction of electric field at that point.
Electric lines of force start from a positive charge and end on a negative charge.
Electric lines of force leave or enter the charged surface normally.
Electric lines of force cannot pass through a conductor. This means that electric field inside a conductor is zero.
Electric lines of force can never intersect each other. In case the two electric lines of force intersect each other at a point, then two tangents can be drawn at that point. This would mean two directions of electric field at that point which is impossible.
Electric lines of force have the tendency to contract in length. This explains attraction between oppositely charged bodies.
Electric lines of force have the tendency to expand laterally i.e. they tend to separate from each other in the direction perpendicular to their lengths. This explains repulsion between two like charges.

## Slide 11: Electric Intensity or Field Strength (E)
The intensity of electric field at any point is determined by the force acting on a unit positive charge placed at that point.
Electric intensity (or field strength) at a point in an electric field is the force acting on a unit positive charge placed at that point. Its direction is the direction along which the force acts.

## Slide 12: Electric Intensity or Field Strength (E)
If a charge of 2 coulombs placed at a point in an electric field experiences a force of 10N, then electric intensity at that point will be 10/2 = 5N/C.
The following points may be noted carefully :
  Since electric intensity is a force, it is a vector quantity possessing both magnitude and direction.
  Electric intensity can also be described in terms of lines of force. Where the lines of force are close together, the intensity is high and where the lines of force are widely separated, intensity will be low.
  Electric intensity can also be expressed in V/m. 1 V/m = 1 N/C

## Slide 13: Electric intensity due to a point charge
The value of electric intensity at any point in an electric field due to a point charge can be calculated by Coulomb’s laws.

## Slide 14: Electric intensity due to a point charge
Note the direction of electric intensity. It is acting radially away from + Q. For a negative charge (i.e. − Q), its direction would have been radially towards the charge.
The electric field intensity in vector form is given as :
where d is a unit vector directed from + Q to + 1C

## Slide 15: Electric field intensity due to a group of point charges
The resultant (or net) electric field intensity at a point due to a group of point charges can be found by applying superposition principle.
Thus electric field intensity at a point P due to n point charges (q1, q2, q3 ... qn) is equal to the
vector sum of electric field intensities due to q1, q2, q3 .... qn at point P i.e.

## Slide 16: Electric Flux (ψ)
Electric flux is a measure of electric lines of force.
The greater the electric flux passing through an area, the greater is the number of electric lines of force passing through that area and vice-versa.
The charge on each plate is Q coulombs so that electric flux between the plates is

## Slide 17: Electric Flux (ψ)
Suppose there is a charge of Q coulombs in a medium of absolute permittivity(=0r) wherer is the relative permittivity of the medium. Then number of electric lines of force N produced by this charge is
The electric flux through a surface area has maximum value when the surface is perpendicular to the electric field.
The electric flux through the surface is zero when the surface is parallel to the electric field.

## Slide 18: Electric Flux Density (D)
The electric flux density at any section in an electric field is the electric flux crossing normally per unit area of that section i.e.
Electric flux density is a vector quantity; possessing both magnitude and direction. Its direction is the same as the direction of electric intensity.

## Slide 19: Relation between D and E
Hence flux density at any point in an electric field is ε0 εr times the electric intensity at that point.
The electric flux density (D) is also called electric displacement.

## Slide 20: Relation between D and E
It may be noted that D and E are vector quantities having magnitude and direction. Therefore, in vector form,
The direction of D at every point is the same as that of E but its magnitude is D = Ɛ0ƐrE.
The value of E depends upon the permittivity Ɛ (= Ɛ0Ɛr) of the surrounding medium, that of D is independent of it.
Electric flux density (D) is directly related to electric field intensity (E); permittivity Ɛ (= Ɛ0Ɛr) of the medium being the factor by which one quantity differs from the other.

## Slide 21: Relation between D and E
The importance of relation D = Ɛ0ƐrE lies in the fact that it relates density concept to intensity concept.
Electric intensity at a point is also defined as equal to the electric lines of force passing normally through a unit cross-sectional area at that point. If Q coulombs is the charge, then number of electric lines of force produced by it is Q/Ɛ. If these lines fall normally on area A m2 surrounding the point, then electric intensity E at the point is

## Slide 22: Electric Potential Energy
Like earth’s gravitational field, every charge (+ Q) has electric field which theoretically extends upto infinity.
If a small positive test charge + q0 is placed in this electric field, the test charge will experience a force of repulsion.
If test charge + q0 is moved towards + Q, work will have to be done against the force of repulsion. This work done is stored in + q0 in the form of potential energy.
We say the charge + q0 has electric potential energy.
The electric potential energy of + q0 depends upon its position in the electric field ; being zero if q0 is situated at infinity.

## Slide 23: Electric Potential Energy
From the above discussion, it follows that just as a mass has mechanical potential energy in the gravitational field, similarly a charge has electric potential energy in the electric field.
The electric potential energy of a charge is positive or negative depending upon the kind of charge.

## Slide 24: Electric Potential
Just as we define electric field intensity as the force per unit charge, similarly electric potential is defined as the electric potential energy per unit charge.

## Slide 25: Electric Potential
Unit. The SI unit of electric potential is volt and may be defined as under :
The electric potential at a point in an electric field is 1 volt if 1 joule of work is done in bringing a unit positive charge (i.e. + 1 C) from infinity to that point against the electric field.
Thus when we say that potential at a point in an electric field is +5V, it simply means that 5 joules of work has been done in bringing a unit positive charge from infinity to that point.

## Slide 26: Electric Potential Difference
The potential difference between two points is the amount of work done in moving a unit positive charge (i.e. + 1C) from the point of lower potential to the point of higher potential.
The SI unit of potential difference is volt and may be defined as under :
The p.d. between two points is 1 V if 1 joule of work is done in bringing a unit positive charge (i.e. + 1 C) from the point of lower potential to the point of higher potential.

## Slide 27: Potential at a Point Due to a Point Charge
The force acting on unit charge (i.e. electric intensity) at distance x is given by;
If this unit positive charge at A is moved through a small distance dx towards the charge +Q, then
work done is given by;

## Slide 28: Potential at a Point Due to a Point Charge

## Slide 29: Potential at a Point Due to a Point Charge
The following points may be noted carefully :
  The potential varies inversely with the distance d from the point charge Q. If the distance is increased three times, the potential is reduced one-third of its value and so on.
  Electric potential is a scalar quantity.
  At d = ∞ in air/vacuum, VP = 9 × 109 q/ ∞ = 0.
  If Q is positive, then potential at P is *positive. On the other hand, if Q is negative, then potential at P is negative.

## Slide 30: Potential at a Point Due to Group of Point Charges

## Slide 31: Potential Gradient
The change of potential per unit distance is called potential gradient i.e. P. G. = (V2-V1)/S
The unit of potential gradient will be volts/m.
Consider a charge +Q and let there be two points A and B situated S metres apart in its electric field as shown in figure.
Clearly, potential at point A is more than the potential at point B. If distance S is small, then the electric intensity will be approximately the same in this small distance. Let it be E newtons/coulomb.
It means that a force of E newtons will act on a unit positive charge (i.e. + 1C) placed anywhere between A and B. If a unit positive charge is moved from B to A, then work done to do so is given by ;

## Slide 32: Potential Gradient
Hence electric intensity at a point is numerically equal to the potential gradient at that point.
Since electric intensity is numerically equal to potential gradient at any point, both must be measured in the same units. Clearly, electric intensity can also be measured in V/m.